## Slide 1
Differential GNSS
for RPO mission
Proposed implementation of an onboard CDGPS
Based on O. Montenbruck and S. D’Amico, “GPS Based Relative Navigation”, chap. 5
Tango
Mango
Notes: Share my understanding of the need, [purpose]
algorithm architecture, [imAgined]
validation plan,
PRISMA, TanDEM-X. [cAïted]

## Slide 2
02
CONTEXT
The need: mm/cm-level relative positioning
2 / 10
5–10 cm
Absolute accuracy, single satellite, depending on timeliness and hardware
< 10 cm
Real-time onboard relative navigation, PRISMA (3D rms, most scenarios)
< 1 mm
Post-processed GRACE baseline vs K-band ranging; 1 mm spec on TanDEM-X
Principle. Differencing the phase of the same GNSS signal received by Tango and Mango removes common errors (satellite clock, ephemerides, and ionosphere on short baselines) and leaves the relative geometry.
Sizing rule (chap. 5)
Control 10× finer than the formation size; navigation 10× finer than control.
Notes: absolute strongly depends on timeliness and hardware;
relative navigation benefits from common-error cancellation, reaches cm in real time and mm offline;
Orders of magnitude gives goals 100x formation size and navigation
TanDEM-X pas autonome, peu de maneouvre, principalement validation sol, fait pour SAR interferométric surtout
K-band ranging is the instrument of GRACE

## Slide 3
03
MEASUREMENT MODEL eq. 5.2
One equation, one strategy per term
3 / 10
Ionosphere
Removed by the Tango − Mango difference (< 1 km); otherwise GRAPHIC / Lear
GNSS satellite clock
Removed by the receiver–receiver difference
Receiver clock
Removed by double difference (≥ 2 common satellites)
Phase wind-up / antenna
Zero if antennas share the same attitude; otherwise model + calibration
Geometry
Estimated: Kalman filter + orbital dynamics
Integer ambiguity
Estimated: LAMBDA / wide-lane, after r has converged
Noise, multipath, events
Detection, KPIs, robustness (slide 9)
■ removed by differencing ■ to be estimated or modelled
Notes: common thread differential algorithm
; one term, one strategy; SORT :
grey strongly reduced through differencing,
coral is what I build;
ionosphere flips sign between code and phase, hence GRAPHIC -> group decrease through ionosphere and phase velocity (frequency of carrier signal) increase through ionosphere.

## Slide 4
04
OVERVIEW
One Kalman filter for both satellites
4 / 10
1
Measurements
GNSS code + phase, Tom and Jerry
2
Pre-processing
Visibility, cycle slips, synchronisation
3
Differencing
Single, then double difference
4
KF + dynamics
Position, velocity, empirical accel.
5
Ambiguities
Float → integer (LAMBDA / WL-NL)
Chosen approach, as on PRISMA
A single filter on the absolute states of both satellites. GRAPHIC and single-difference phases are processed together, so no explicit relative state is needed, common visibility is not a strict prerequisite, and each satellite’s dynamics are propagated separately. Update every 30 s.
Notes: Each receives GNSS
Jerry transmits through inter-satellite link
Tom identify the GPS satellites commonly tracked and from single and double difference
These are processed inside a common Kalman filter
Estimate absolute states of both satellites simultaneously
common visibility mandatory.
Least-squares Ambiguity Decorrelation Adjustment (covariance)
Wide Lane-Narrow Lane (pseudorange, for double_frequency receivers)

## Slide 5
05
RECEIVER CLOCK c·δt
Co-visibility: what each step needs
5 / 10
≥ 1
common satellite
to form a single-difference phase
≥ 2
common satellites
to form a double difference: c·δt cancels, integers can be fixed
Below that: undifferenced GRAPHIC keeps both absolute states, and so the relative state, alive.
Detection
Satellites tracked by Tango and Mango at each epoch, and their intersection
Lookup table
Full GPS and Galileo constellation, health from NANU / NAGU notices
Alert
Fewer than 2 common satellites: flag, suspend fixing, keep float
Validation
Cross-check against a trajectory visualisation tool on pass scenarios
Notes: Flight plan
Juste detection et alert
fallback to GRAPHIC or the common kalman filter -> let alive;

## Slide 6
06
GEOMETRY |r − r_GPS|
Kalman, dynamics, real measurements
6 / 10
Is the flight plan enough? No. The model predicts, the measurements correct.
1 Prediction
Numerical integration of each orbit
Geopotential, drag, Sun/Moon, SRP, empirical accelerations
Thrusts known from the flight plan
2 Correction
Residuals = measured − modelled
Pseudorange, noise ~0.5 m
Phase, noise ~1 mm, ambiguous
Thrust tuning on PRISMA: measurement σ × ~10 during frequent thrusting; manoeuvre states estimated online.
Notes: Empirical acceleration represent perturbations not captured by the force model.
->as slowly varying states : filter remains accurate even modelling is imperfect.
Correction : sensitive to noise & start drifting.
SRP = solar radiation pressure = space weather
Geopotential = gravité terrestre

## Slide 7
07
INTEGER AMBIGUITY λ·A
LAMBDA and safeguards
7 / 10
1
Converge
Filter converged on r before any attempt
2
Float
Ambiguities estimated as real numbers
3
Fix
LAMBDA with validation, or WL/NL rounding (eq. 5.9)
4
Monitor
Cycle slip: reset only the ambiguities concerned
< 1 cm
Integers fixed
PRISMA ground baseline, clamped config. (3D rms)
5 cm
Float only
Same test, float ambiguities (3D rms)
Heavy manoeuvres: processing reverts to float only. Only the double difference is integer, for a properly designed receiver.
Notes: phase provide millimetric precision : within a single carrier cycle.
cycles the signal has travelled from
This unknown integer number = phase ambiguity.
converge first; float then integer; only the double difference is integer; LAMBDA with validation, 1 cm vs 5 cm float;
float only during heavy manoeuvres.

## Slide 8
08
ANTENNA λ·Ψ
Radiation pattern and phase centre
8 / 10
azimuth × elevation grid
Gain pattern
Amplitude vs direction → C/N0, tracking quality
Phase centre variations
Apparent phase-centre offset vs direction → phase error
Same characterisation campaign, no conversion formula between the two.
My approach
Gather: antenna spec and measured gain / phase pattern from the integration team
Tabulate: phase correction on an az/el grid, interpolated with NumPy / SciPy
Calibrate: on ground and in flight: PCV up to 10 mm even with a choke ring
Notes: 2 phenomena : gain pattern (from directions)
Carrier phase processing assumes that signal received at a specific reference point (phase center)
In pratice, it changes with the direction of teh incoming signal -> error and calibration
PCV = phase center variation
Choke-ring antenna : concentric metal rings, delayed copies, enable corrections. It is an antenna designed for high-precision GNSS.

## Slide 9
09
NOISE AND EVENTS ε
Proving the algorithm holds
9 / 10
Measurement threats
Manoeuvre execution, attitude errors
Multipath, phase pattern distortions
Data gaps, tumbling, safe mode
Jamming
System threats
SEU, SEL → EDAC, latch-up protection; receivers off to limit SEE → robust filter settings
Proposed KPIs
Relative position and velocity RMS (3D)
DD phase residuals, target ~mm
Fixing rate, cycle-slip count
Common satellites, convergence time
C/N0 on Tom and Jerry (jamming)
My proposal
Doppler consistency
Phase rate must match the predicted relative velocity. A phase jump without a velocity jump is a cycle slip, not real motion.
Notes: manoeuvres, multipath, data gaps, radiation
Code protection
where we are in the signal cycle but not how many cycles were missed during the interruption
SEE = SE effect : radiation
SEU = SE upset (bit flip)
SEL = SE latch-up (short circuit)
EDAC = Error Detection And Correction (code)

## Slide 10
10
FROM DAY ONE
First concrete actions
1
KPI set and scenarios
Indicators and validation cases defined first
2
Work environment
Python, IDE, InfluxDB + Grafana, GNU Radio
3
GNSS database
Store GPS / Galileo data, automatic plots
4
Signals state of the art
Civil signals and frequencies available today
5
TLE retrieval
Automated for long-lived satellites
Objective
< 10 cm
in real time, onboard (3D rms)
~1 mm in post-processing
Proven in flight by PRISMA and TanDEM-X, within reach for Tango & Mango.
10 / 10
Notes: below 10 cm in real time, mm offline